## Slide 1: Data Center Demand Response: Coordinating IT and the Smart Grid
Zhenhua Liu
zhenhua@caltech.edu
California Institute of Technology
December 18, 2013
Acknowledgements:
Adam Wierman1, Steven Low1, Yuan Chen2, Minghong Lin1, Lachlan Andrew3, , Cullen Bash2, Niangjun Chen1, Ben Razon1, Iris Liu1
1California Institute of Technology, 2HP Labs, 3Swinburne University of Technology
Notes: job market

## Slide 2
Sustainable IT
IT for sustainability
Energy efficiency of IT system
IT as a demand response provider
Notes: broader impacts

## Slide 3: Renewables are coming
Cumulative capacity has grown by 72% from 2000–2011
Wind and solar grow fastest (13x and 51x)
Source: Gelman, R. (2012). 2011 Renewable Energy Data Book (Book). Energy Efficiency & Renewable Energy (EERE)
Worldwide Renewable Electricity Capacity
Notes: increase in renewable

## Slide 4: Challenges with renewables
Generation
Time
Power
12 AM
12 AM
Generation = Demand
at all times
at all locations
Demand
Key constraint:
predictable
controllable
low uncertainty
Generation follows Demand
Notes: traditional approach: generation follows supply

## Slide 5: Challenges with renewables
Generation
Generation = Demand
at all times
at all locations
Demand
Key constraint:
responsive
less controllable
high uncertainty
Demand follows Generation
(to some extent)
expensive
Notes: challenges with renewable integration

## Slide 6: Need huge growth in demand response
Data centers are a promising option
Wind and Solar capacities are growing 15~40% per year
large loads: 500kW~50MW each
increasing fast: 10~15% per year
significant flexibilities
Notes: Others vs DC

## Slide 7: Data center flexibilities
cooling, lighting, …
  5% of consumption can be shed in 2 min [LBNL2012]
  10% of consumption can be shed in 20 min [LBNL2012]
workload management
  Temporal demand shaping [Sigmetrics12][3 patents]
  HP Net-Zero data center, 2013 Computerworld Honors Laureate
  Geographical load balancing [Sigmetrics11][GreenMetrics11][IGCC12]
  Best student paper award at ACM GreenMetrics 2011
  Best paper award at IEEE Green Computing 2012
  Pick of the Month in the IEEE STC on Sustainable Computing
onsite backup generators & storage
Notes: previous work: design & implementation, distributed and online algorithms with theoretical guarantee

## Slide 8: Geographical load balancing
Notes: power and cooling
spatial flexibility
future: robustness when adding new data center or failure

## Slide 9: Data center flexibilities
cooling, lighting, …
  5% of consumption can be shed in 2 min [LBNL2012]
  10% of consumption can be shed in 20 min [LBNL2012]
workload management
  Temporal demand shaping [Sigmetrics12][3 patents]
  HP Net-Zero data center, 2013 Computerworld Honors Laureate
  Geographical load balancing [Sigmetrics11][GreenMetrics11][IGCC12]
  Best student paper award at ACM GreenMetrics 2011
  Best paper award at IEEE Green Computing 2012
  Pick of the Month in the IEEE STC on Sustainable Computing
onsite backup generators & storage
great opportunities

## Slide 10: Data center demand response today
coincident peak pricing (CPP)
time
customer power usage
system peak hour
(decided by utility)
coincident peak demand
customer’s peak demand
Many programs
Time of use (ToU) pricing
  Wholesale market
  Ancillary service market
Monthly bill = fixed charge + usage charge + peak charge + coincident peak charge
Notes: CPP is popular
how CPP works

## Slide 11: CPP in practice
Rates at Fort-Collins Utilities, Colorado, USA
CP is very important!
fixed charge: $101.92/month
usage charge rate: $0.0245/kWh
peak charge rate: $4.75/kW
coincident peak (CP) charge rate: $12.61/kW
Example: average demand 10MW, peak demand 15MW, CP demand 14MW
Monthly bill = fixed charge + usage charge + peak charge + coincident peak charge
$101.92
$176,400
$71,250
$176,540
Notes: CPP is very important

## Slide 12: DC management is challenging
Uncertainties in CP
only known at the end of the month
Participating CPP program is risky!
algorithm design
Notes: challenge

## Slide 13
mind f(d; t)
expected cost optimization
data mining for patterns
less accurate with renewables
robust optimization
mind Et[f(d; t)]
mind maxt [f(d; t)]
online algorithm
optimal competitive ratio
Extensions
warning signals
backup generator & local renewables
workload & renewable prediction errors
Notes: what is f
two approaches
performance guarantee
extension

## Slide 14
mind f(d; t)
expected cost optimization
robust optimization
Time
Power
12 AM
12 AM
periods with high probability to be CP
Time
Power
12 AM
12 AM
make the demand flat
Limited demand response
market design
Notes: limited demand response

## Slide 15: Potential of data center demand response
Goal: minimize voltage violation with large PV generation
20MW DC
3MWh storage
=
voltage violation rate
with 20% flexibility
optimal location & fast charge rate
Notes: great potential from the society’s perspective

## Slide 16: Pricing data center demand response
supply function si(p)

## Slide 17: Pricing data center demand response
efficiency loss due to user strategic behavior [XLL2013]
market-clearing price p
supply function bidding
but when we have data centers …
works well when no user has large market power

## Slide 18: Pricing data center demand response
price p
prediction-based pricing
supply function

## Slide 19: Pricing data center demand response
prediction-based pricing
supply si(p)
efficiency loss is independent of market power
but depends on prediction accuracy
parameter in supply function
for quadratic cost function

## Slide 20
supply function bidding
prediction-based pricing
vs
efficiency loss depends on market power
efficiency loss depends on prediction accuracy
supply function bidding
prediction-based pricing
supply function bidding
prediction-based pricing

## Slide 21
supply function bidding
prediction-based pricing
vs
incorporating power network
value of location
optimal power flow
learning from user response
exploitation vs exploration
theory of quantization
[BSXY2012]
Pick of prices during learning stage
Design demand response “menu”
Notes: future work
connection

## Slide 22
demand response
flexibilities
cloud platform

## Slide 23
Thank you!

## Slide 24: References
[LBNL2012] Ghatikar, Girish, et al. "Demand response opportunities and enabling technologies for data centers: Findings from field studies." LBNL-5763E. 2012.
[XLL2013] Yunjian Xu, Lina Li, Steven Low. “On the Eciency of Parameterized Supply Function Bidding with Capacity Constraints”. 2013.
[BSXY2012] Bergemann, Dirk, et al. "Multi-dimensional mechanism design with limited information." Proceedings of the 13th ACM Conference on Electronic Commerce. ACM, 2012.

## Slide 25: Model for prediction based pricing
user
for each realization
cost function
supply
utility
penalty
social objective
offline optimal

## Slide 26: Model for prediction based pricing
utility
penalty
social objective
offline optimal
performance evaluation
competitive ratio
Theorem