## Slide 1: Wave and Surge Structural Damage to Shorefront Residential Properties from Hurricane Sandy
Andrew Kennedy
University of Notre Dame
Ning Lin
Princeton University
NSF CMMI 1314612
NSF CMMI 1314649

## Slide 2: Project Overview
Two major goals:
  To collect perishable data on residential building damage levels, failure modes, and building characteristics (elevation, specific connections/members failed, age)
  To find damage gradients, and to identify and quantify their causes
Region around Ortley Beach/Seaside Park/Pelican Island, NJ
Five day field data collection, 5-8 field workers at a time
Supplemented by aerial and satellite photos, publicly available records, environmental data, numerical modelling

## Slide 3: Geographic Overview
Ortley Beach
High waves, surge
Pelican Island
Smaller Waves
South Seaside Park
Largely Protected
Rutgers

## Slide 4: Data Collected
House-by-house survey in target areas
  Lat/Long
  House properties (wood/RC/#stories)
  Geotagged photos
  Damage descriptions and levels
    Many subcategories
  House floor elevation
Supplemental info
  House age
  Assessed value/losses (from tax records)
  Aerial/satellite photos
  Measured environmental data during storm
Numerical modeling of hydrodynamics
  Still in progress
■ 0-33% Damage ■ 33-66% ■ 67-100%

## Slide 5: Sample Photos (of ~3900)
Exposed Areas of Ortley Beach
Pelican Island

## Slide 6
Sheltered Behind Dune South Seaside Park
Exposed to Surge but not Waves
Ortley New Construction
Ortley Sliding Failure

## Slide 7: Houses far from Ocean Survived Better
Chart: Year of Construction and Distance From Ocean of Observed Structures
Some trends clear, but distance and age are not only factors
Need hydrodynamic data to distinguish between conditions encountered by structure

## Slide 8: Collaborative Geospatial-Enabled Data Management
Web-based system under development to collect all types of Sandy (and other) data sources under one umbrella
  Geospatial Format – Grass GIS-based
  Searchable Database
    Measured data: damage, HWM, etc
    Models
    Links to external sources
Data sharing and collaboration
Will also be able to run some models
Will be inviting others to join as site development matures

## Slide 9
Data Points and Permanent Measuring Stations For Sandy

## Slide 10
Part of Ortley Beach Dataset and Sample Popup

## Slide 11
Example of External USGS HWM Data Point

## Slide 12: Key Findings so Far
Poor connections on (mostly) older houses leads to house sliding
  Also on some newer houses
Major wave damage near shoreline, decreasing inland
Minor wind damage: mostly shingles, a few debris impacts
Dune sheltering of extreme importance
Scattered scour damage in region
Standardization and consistency of damage estimates remains fluid

## Slide 13: Continuing Work
Increasing datasets
  Mainly survived/failed using satellite data
Hydrodynamic Simulations
  SWAN+ADCIRC (Westerink Group)
  Problems with lidar elevations post-storm
Integrating Sandy datasets online
Damage reporting standards
Link to other storms: Ike in particular
Fragility Curves
  Damage state vs hydrodynamics, building properties, etc.

## Slide 14: Fragility Example from Hurricane Ike
Fragility (failure) increases strongly with increasing wave heights
Older houses significantly more fragile
Higher house elevations (higher FB) survive better
Lower Elevations
Higher Elevations

## Slide 15: Questions?
Thanks to Tori Tomiczek, Margaret Owensby, Rich Estes, Luca Nagy, Trenton Jackson, Emmi Yonekura, Jonathan Glassman