## Slide 1: A SOFT Way for OpenFlow Interoperability Testing
Marco Canini
TU Berlin / T-Labs
[CoNEXT’12]

## Slide 2: First: my view on SDN
Today
Reliability
Performance
SDN: A role for software engineering
and formal methods to improve reliability
Evolved
Simple to manage and program
Less complexity
Deterministic and verifiable behavior

## Slide 3: Reduce the risk of bugs!

## Slide 4: Software Faults
Will make communication unreliable
Major hurdle for success of SDN
We need effective ways to validate SDN networks

## Slide 5
Network topology
Correctness properties (e.g., no loops)
Traces of property violations
Input
Output
NICE [NSDI’12]
Systematic state-space exploration
Unmodified OpenFlow program

## Slide 6
Okay, now back to OpenFlow Interoperability Testing

## Slide 7: Interoperability at Deployment Time
Release
OpenFlow program
OpenFlow messages
One OpenFlow API specification…
Are OF switches interoperable?
Interop is critical for the success of SDN

## Slide 8: Interop: How Hard Can It Be?
OF Switch
Inputs
Hardware correctness is formally verified
Packets
OpenFlow messages
“Forwarding” interface
OpenFlow interface
ASIC switch chip
OS
OpenFlow Agent
Likely source of OpenFlow interop issues
Flow Table Hardware Abstraction Layer

## Slide 9: OpenFlow Software Agent
Specifications
Rapid flux (3 revisions in ~ 1 year)
Ambiguities
Specifications  Implementation
Implementation freedom
Vendors may not follow the specs
Testing, testing and testing…
Switch software is not provably correct 

## Slide 10: Interoperability Event
Gather various vendors
Hook up switches and controllers
Create and run test cases
See what breaks and fix it
Very high manual effort
Test cases are not exhaustive
It is not a one time thing

## Slide 11: Automating Interop Testing
Insight: systematically crosscheck OF implementations

## Slide 12: The 10,000 foot view
OF Agent 1
Test inputs
Input-driven execution
Observable behaviors
Inconsistency!
OF Agent 2
Problem I: What inputs should we use?

## Slide 13: Symbolic Execution
If ( p == OFPP_CTRL )
send_to_ctrl ( )
else if ( p < 25 )
send_to_port( p )
else
error( BAD_PORT )
p
p == OFPP_CTRL
p != OFPP_CTRL
p < 25
p >= 25
send_to_ctrl ( )
send_to_port( p )
error
Path condition:
p >= 25 & p != OFPP_CTRL
FWD
ERR
CTRL
ERR
p:
1
24
25
65535
OFPP_CTRL
Problem II: Path explosion

## Slide 14: Challenges
Manage test inputs and coverage efficiently
Capture behaviors
Avoid simultaneous access to all code

## Slide 15: SOFT (Systematic OpenFlow Testing)
OF Agent 1
Test inputs
Input-driven execution
Observable behaviors
OF Agent 2
Phase 2
Phase 1
Determine mapping inputs  behaviors through symbolic execution
Identify inconsistencies
Automated solution to interop testing
Systematic code coverage
No simultaneous access to all agents

## Slide 16: Structured Inputs
...
*
*
*
*
*
*
*
*
*
*
*
*
FLOW
MOD
N1
STAT
REQ
N2
1.0
1.0
Further reductions
Some inputs are independent
Many inputs are entirely concrete
Small number of messages
Concrete values at cost of coverage
C1
C2

## Slide 17: Capturing Behaviors
Externally observable outputs
  OpenFlow reply messages
  Data plane packets
  Normalize harmless nondeterminism (e.g., Buffer IDs)
Internal state changes affect successive inputs
  Use concrete probe packets

## Slide 18: Example
If ( p == OFPP_CTRL )
send_to_ctrl ( )
else if ( p < 25 )
send_to_port( p )
else
error( BAD_PORT )
if ( p < 25 )
send_to_port( p )
else
error( BAD_PORT )
Agent 1
Agent 2
FWD
ERR
CTRL
ERR
p:
1
24
25
65535
OFPP_CTRL
FWD
ERR
p:
1
24
25
65535

## Slide 19: N-version Comparison
If ( p == OFPP_CTRL )
send_to_ctrl ( )
else if ( p < 25 )
send_to_port( p )
else
error( BAD_PORT )
if ( p < 25 )
send_to_port( p )
else
error( BAD_PORT )
Agent 1
Agent 2
FWD
ERR
CTRL
ERR
p:
1
24
25
65535
OFPP_CTRL
p:
FWD
ERR
1
24
25
65535

## Slide 20: N-version Comparison
Is there an input subspace that causes two distinct behaviors?
FWD
ERR
CTRL
ERR
p:
1
24
25
65535
OFPP_CTRL
FWD
ERR
No false positives
Agent 1
Agent 2

## Slide 21: Limitations
Short sequences of inputs
  Unable to find problems with a complex state
Is an inconsistency harmless?
  Can it affect the controller?
  How to test all initial configurations?
    Agent’s behavior depends on initial config

## Slide 22: Prototype & Evaluation
SOFT prototype built on top of Cloud9/Klee
Compared
  OpenFlow 1.0 Reference Switch (55k LoC)
  Open VSwitch 1.0.0 (80k LoC)
Input Sequences containing 1 - 4 messages

## Slide 23: Does SOFT Work?
Found 7 classes of inconsistencies
Mostly related to message validation
Result of underspecification
  No expected behavior in the specification
  Inconsistent interpretation of the specification

## Slide 24: Inconsistency - Example
FlowMod message
Modify VLAN to value greater than 212
Forward packet
Reference Implementation
Trim VLAN value to 12 bits
Install the rule
Open VSwitch
Silently ignore the message
Network in 2 different states
Which one is assumed by the controller?

## Slide 25: Concretizing Tradeoffs
Chart: 
| 12.0 | 193.0
Coverage | 0.406 | 0.3732
Chart: 
| 1.0
Column1 | 0
Y-Values | 0.4293
Fully
Symbolic
28h

## Slide 26: Conclusions
SOFT automates interoperability
testing of OpenFlow Agents
Also useful for:
Regression testing
Specification improvements
Systematic code coverage
No simultaneous access to all agents

## Slide 27: Thanks
Peter Perešíni (EPFL)
Maciej Kuźniar (EPFL)
Daniele Venzano (EPFL)
Dejan Kostić (EPFL  IMDEA Networks)

## Slide 28: Thank you!
SOFT automates interoperability
testing of OpenFlow Agents
Also useful for:
Regression testing
Specification improvements
Systematic code coverage
No simultaneous access to all agents