## Slide 1: SDN: New Approach to Networking
Guru Parulkar
parulkar@stanford.edu
http://onrc.net/

## Slide 2: Key Takeaways
SDN is hot and has captured industry’s imagination
SDN is not just a feature but a new way of thinking
  SDN abstractions and what they enable
SDN is in an early stage of development
  Lot of opportunities to shape it
  Our opportunity to impact practice of networking

## Slide 3
“OpenFlow and Software Defined Networking (SDN) are not only here to stay, but they will define the future of networking.”
Network World, 10/18/2011
“SDN: Your Next Network
SDN has the potential to bring new levels of automation and efficiency to networks.”
October 2012, Information Week

## Slide 4
70+ companies joined ONF in a year
Notes: More than 65 companies joined ONF in a year.
Let us take a minute to browse the list.

## Slide 6
70+ companies from across the industry
Notes: These companies are from across the networking and cloud infrastructure industry.
They are small and large companies
They are Enterprise, carriers, and web service providers
They are chip, equipment and different types of software vendors
Essentially OpenFlow and SDN have captured industry’s imagination and different players across the ecosystem see the value.
Not only that OpenFlow and SDN are becoming more real.

## Slide 7
SDN Exhibits by 20+ Companies at ONS-12
SDN Product Awards at Interop (NEC)
Notes: Another good indication is the set of exhibits by the companies.
There are over 20 companies that are doing exhibits of OpenFlow and SDN technologies, products, and services at ONS.

## Slide 8
“HP Advances Software-Defined Networks with Integrated Infrastructure, Controller and Application Solutions,” HP, October 2, 2012
“Cisco ends the SDN suspense, Unveils Cisco ONE architecture and strategy for instilling programmability into its network gear,” Jim Duffy, Network World, June 13, 2012 11:32 AM ET
“Alcatel-Lucent Joins Cisco, HP, Others in SDN Push,” Jeffrey Burt | Posted 2012-12-01, eWeek
“Brocade bolsters its SDN game, buys Vyatta,” ZDNet, November 5, 2012
“Big Switch Networks Ships First Open Software-Defined Networking Product Suite to Accelerate Network Transformation,” Big Switch, November 13, 2012

## Slide 9
VMWare acquires Nicira
Brocade acquires Vyatta
Cisco setups Insieme as a spin-in
Cisco acquires Cariden
SDN startups: Big Switch, PlumGrid, Vello, Contrail, …

## Slide 10: What is the problem?

## Slide 11: Problem with Internet Infrastructure?
Million of lines of source code
6000+ RFCs
Billions of gates
Bloated
Power Hungry
Vertically integrated, complex, closed, proprietary Not suitable for experimental ideas
Specialized Packet Forwarding Hardware
Operating
System
Feature
Feature
Routing, management, mobility management, access control, VPNs, …
Not good for network owners & users; Not good for researchers.

## Slide 12: Problem: No Abstractions for Control Plane
Forwarding
OS
Forwarding
OS
Forwarding
OS
Addition of a new function to the network
  Highly complex distributed system problem
Networks too difficult to program and to reason about
  no good abstractions and interfaces
Router/Switch/Appliance
Router/Switch/Appliance
Router/Switch/Appliance
Distributed
Network Functions
State Distribution Mechanism
Not good for even network vendors

## Slide 13: Why Does Verizon Care?
© 2011 Verizon. All Rights Reserved.
Stu Elby @Open Networking Summit
http://OpenNetSummit.org/

## Slide 14: Enterprise Networking
Enterprise network operators want..
Firewall and access control
Delegate management to departments
Lots of VLANs that stretch across buildings
By-pass bottlenecks/check points for specific applications
Host web services with load balancing
Easy guest wireless access with security
BYOD (Bring Your Own Device) challenges
And more
How do they do it today?

## Slide 15: Enterprise Network: Today’s solution
Proliferation of appliances
Increased management complexity
  Device oriented management
  Each device type has its own management
High Capex, high Opex
Too much reliance on vendors
Load balancer
IDS
Firewall
Load balancer
IDS
Firewall
ACL
ACL
ACL
ACL
ACL

## Slide 16: Data Center Provider Today
Assign VMs to any server without considering L2/L3 scalability
Support multiple tenants with lots of VMs interconnected
Support each tenant with its own customized network for VMs: topology, bandwidth, security, load-balancing
And everything is dynamic
Load balancers
Firewalls
IDS’s
?
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
Tenant-A
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
Tenant-B
VM
VM
VM
VM
VM
VM
VM
VM
Tenant-C
Vendors find it hard to develop solutions
Network is the long pole

## Slide 17: What is SDN? How does it help?

## Slide 18: Software-Defined Network with Key Abstractions in the Control Plane
Routing
TE
Network OS
Open interface (OpenFlow) to Forwarding Abstraction: L1/L2/L3
Well-defined open API
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Separation of
Data and Control
Plane
Network Map
Abstraction
Mobility
Programmable
Basestation

## Slide 19: Software Defined Network with Virtualization
Network OS
Global Network View
Abstract Network Model
Control Program
Network Virtualization

## Slide 20: Stanford/Berkeley SDN Activities With Partners
2007
2011
2008
2009
2010
Ethane
Demo
Deployment
Platform
Development
OpenFlow Spec
v0.8.9
v1.0
v1.1
Reference Switch
NetFPGA
Software
Network OS
NOX
SNAC
Beacon
Virtualization
FlowVisor
FlowVisor (Java)
Tools
Test Suite
oftrace
Mininet
Measurement tools
GENI software suite
Expedient/Opt-in Manager/FOAM
Stanford University
~45 switch/APs ~25user
In McKeown Group
CIS/EE Building
Production Network
US R&E Community
GENI: 8 Universities + Internet2 + NLR
Many other campuses
Other countries
Over 68 countries
(Europe, Japan, China, Korea,
Brazil, etc.)
VM Migration
(Best Demo)
Trans-Pacific
VM Migration
Baby GENI
Nation Wide GENI
“The OpenFlow Show”
– IT World
SDN Concept
(Best Demo)
SIGCOMM08
GEC3
SIGCOMM09
GEC6
GEC9
Interop
2011
+Broadcom

## Slide 21
Nation-wide SDN Infrastructure Part of NSF’s GENI
Notes: During 2010, we and our partner universities deployed OPEN networks at 8 campuses and interconnected them by OPEN backbone network within NLR and Internet2.

## Slide 22: SDN Reference

## Slide 23
Example Demonstrations
Onrc.stanford.edu/videos.html

## Slide 24: Carrier Networks Today
They want to offer
VPN Services
Traffic Engineering
And other value added services
Router Operating System
Distributed
Network Functions
IGP- Route Advert, Link-State
TE Label Distribution
VPN-IPv4 Route Advert
E-BGP learned Route Advert
PE Label Distribution
Distributed Network Functions
each with their own
State Distribution Mechanisms
OSPFv2
RSVP-TE
MP-BGP
I-BGP + RR
LDP
State Distribution
Mechanisms
Go to vendors and ask them for solutions:
Vendors find it hard to develop solutions
Providers find it too slow and too expensive to deploy and operate
Providers depend too much on vendors

## Slide 25: Carrier Networks (MPLS) with SDN
Routing
Discovery
Label Distribution
Recovery
Simpler Control Plane
(2)
Simpler
Cheaper
Multi-Vendor
Data Plane
(1)
SWAP
POP
PUSH
Vendor-agnostic Open Interface
NETWORK OPERATING SYSTEM
TE 2.0
Services / Network Applications
(3)
VPN
~4K vs. ~600k lines of code

## Slide 26: Urs Hölzle, SVP, Google at ONS 2012
SDN Early Adopters: Google

## Slide 27: Cloud Provider with SDN
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
Load
Balancing
Firewall
Tenant-A
NETWORK OS
VM
VM
VM
VM
VM
VM
Tenant-B
NETWORK OS
Load
Balancing
IDS
VM
VM
VM
VM
VM
VM
VM
VM
Tenant-C
NETWORK OS
Firewall
IDS
Load
Balancing

## Slide 28
SDN Early Adopters: Data Center Virtualization

## Slide 29: Enterprise Network with SDN
Load balancer
IDS
Firewall
Load balancer
IDS
Firewall
ACL
ACL
ACL
ACL
ACL
NETWORK OPERATING SYSTEM
Load
Balancing
IDS
Access
Control
Policy
Routing
Vender-agnostic Open Interface
Simple, Cheaper
Multi-vendor
Data Plane
Centralized
Control Plane
NETWORK OS
IDS
Access
Control
Financial Department
NETWORK OS
Policy Routing
Research Labs
And you can even delegate control to someone else

## Slide 30: SDN is not just a feature but a new way of thinking: SDN abstractions and what it enables

## Slide 31: SDN Origins
Routing
TE
OpenFlow Controller: Event Based Interface
Open interface (OpenFlow) to Forwarding Abstraction: L1/L2/L3
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Separation of
Data and Control
Plane
Mobility
Packet
Forwarding

## Slide 32: Software Defined Network with Virtualization
Network OS
Global Network View
Abstract Network Model
Control Program
Network Virtualization

## Slide 33
Scott Shenker at 1st ONS in 2011
“The Future of Networking and the Past of Protocols”
Notes: If you haven't seen Scott's talk, you must.
Scott masterfully described the new SDN abstraction for networking.

## Slide 34: How do SDN abstractions help? Network Virtualization Automatic Network Trouble Shooting …

## Slide 35: Making SDNs Work
Nick McKeown
Stanford University
Thanks to: NSF, GPO, Open Networking Research Center (ONRC) Cable Labs, Cisco, DoCoMo, DT, Ericsson, Google, HP, Huawei, Intel, Juniper, NEC, Texas Instruments
2nd Open Networking Summit
http://OpenNetSummit.org/

## Slide 36
With SDN we will:
  Formally verify that our networks are behaving correctly.
  Identify bugs, then systematically track down their root cause.

## Slide 37: SDN Operation
Physical Network
Network OS makes sure the flow entries are installed properly
App
App
App
App
App
Controller
Controller
Virtualization
Network OS (Dist. State Mgmt)
Virtual Network
Virtual Network
Global Network View
Abstract Network View
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
A can talk to B
B can talk to C
A cannot talk to C
Describe the desired
behavior on the
abstracted network view
Virtualization Layer
translate it to Global
Network View

## Slide 38: Network Troubleshooting Enabled by SDN
Global Network View
Network Virtualization
Abstract Network View
Control
Programs
Control
Programs
Control
Programs
Network OS
(1) Static Checking
Is the “policy”
correctly compiled
to the forwarding rules?
(2) Automatic Checking
Is the datapath working
as specified?
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
<Match, Action>
<Match, Action>
<Port == 22, Drop>
<Match, Action>
<Match, Action>
<Match, Action>
(3) Network Debugger
Finding bugs, and their root cause, in an operational network

## Slide 39: Header Space Analysis Based Tools
Peyman Kazemian
Policy
Policy
Policy
Control Plane Logic
Rules
Rules
Rules
Rules
Rules
Rules
Rules
Rules
Header Space Analysis: models forwarding
behavior of network based on these rules.
Hassel,NetPlumber: verify equivalence of policy
and expected end-to-end network behavior.
ATPG: verify correctness of actual data plane behavior by generating test packets based on network rules.
Notes: Before concluding my talk, I want to zoom out a little bit to see the bigger picture of all these tools and how they are related.

## Slide 40
Control Plane
Flow Table State Recorder
Packet
Histories
Troubleshooting Application
NetSight API
add_filter(packet_history_filter, callback)
Incorrect packet modification
Isolation violation
Black holes
Waypoint routing violation
Path length violation
Troubleshooting Application
Troubleshooting Application
Troubleshooting App
Nikhil Handigol

## Slide 41: Troubleshooting Applications
nprof
Hierarchical Network Profiler
ndb
Interactive Network Debugger
netwatch
Live Invariant Monitor
netdump
Network-wide Logger
Notes: Nprof – hierarchically shows the sources of congestion causing traffic in the network.
netdump – Advanced tcpdump that lets you log packets anywhere in the network, with filters on the packet history

## Slide 42: SDN is at the early stage of development Lot of opportunities to shape it

## Slide 43: SDN Opportunities
OF Switch
Open Radio
VIrtualization
Prog/Debug
Systems
Mininet & Tools
Scalability
Reliability
Security
Flow Space
Network Map
Virtual Network
Big Connector
Network OS-wireless
Systems
Abstractions
Xlities
Network OS
Feature
Network OS
OF Switch
OF Switch
OF Switch
OF Switch
Logical Map of Network
Network HyperVisor
Virtual Network
Programming System/Tools
Big Connector
Feature
Feature
OpenRadio

## Slide 44: SDN Opportunities Cont.
Domains of Use
Enterprise Networks
Datacenter Networks
Service Provider Networks
Cellular Networks
Home Networks
OF Switch
Open Radio
FlowVisor
Prog
Systems
Mininet & Tools
Scalability
Reliability
Security
Flow Space
Network Map
Virtual Network
Big Connector
Network OS-wireless
Systems
Abstractions
Xlities
Network OS
OF Switch

## Slide 45: Key Takeaways
SDN is hot and has captured industry’s imagination
SDN is not just a feature but a new way of thinking
  SDN abstractions and what they enable
SDN is in an early stage of development
  Lot of opportunities to shape it
  Our opportunity to impact practice of networking

## Slide 46: Team at Stanford
Nick McKeown, Guido Appenzeller, Nick Bastin, David Erickson, Glen Gibb, Nikhil Handigol, Brandon Heller, TY Huang, Peyman Kazemian, Masayoshi Kobayashi, Jad Naous, Johan van Reijendam, Srini Seetharaman, Rob Sherwood, Dan Talayco, Paul Weissman, Tatsuya Yabe, KK Yap, Yiannis Yiakoumis and many more.
With Scott Shenker and team at Berkeley and Martin Casado at Nicira
Notes: We have a great team… a team of great graduate students, engineers, and post docs. These people deserve all the credit for what I am going to talk about.
We also collaborate with Scott and his team at Berkeley and Martin from Nicira among other people.