## Slide 1: Toward Practical Integration of SDN and Middleboxes
Zafar Qazi, William Tu, Luis Chiang, Stony Brook University
Rui Miao, Minlan Yu
USC
Vyas Sekar
Stony Brook University
Joint work with

## Slide 2
Type of appliance | Number
Firewalls | 166
NIDS | 127
Media gateways | 110
Load balancers | 67
Proxies | 66
VPN gateways | 45
WAN Optimizers | 44
Voice gateways | 11
Total Middleboxes | 636
Total routers | ~900
Middleboxes Galore!
Data from a large enterprise
Survey across 57 network operators
High capital and management costs Little flexibility
Notes: Refer to guru’s slide

## Slide 3: Our past work in MB space
CoMb [NSD1 ‘12]
  Consolidate hardware-software
  Consolidate management
Aplomb [SIGCOMM ‘12]
  Outsource middleboxes to the cloud
NIDS/NIPS Load Balancing [CoNext ‘10 ‘12]
  Network-wide load balancing

## Slide 4: Two crucial missing links
Can we deal with existing middleboxes?
  Legitimate technical and business reasons
  (Over)simplified or assumed away the problem?
Use custom API, not SDN interfaces
  In spite of the obvious parallels
Why haven’t we seen a practical integration
between SDN and existing middleboxes?
“…policy might require packets to pass through an intermediate middlebox….” Casado et al, SIGCOMM ‘07

## Slide 5
Goal of this work
Middleboxes
IDS, Firewall, Load balancer, VPN
WAN optimizer, Proxy, etc
Centralized management
with open interfaces
e.g., NOX/OpenFlow
Centralized management with open interfaces
e.g., NOX/OpenFlow
IDS, Firewall, Load balancer, VPN
WAN optimizer, Proxy, etc

## Slide 6: What this work is NOT
New vision for SDN
New vision for middlebox
A new L4-L7 programmable data plane
New northbound APIs for middleboxes
Look for practical, incremental convergence

## Slide 7: Roadmap
Motivation + Context
Challenges with SDN-MB integration
Promising starts
Reflections..

## Slide 8: Middlebox “policy chain”
S1
S5
S2
S3
S4

*
Firewall
IDS
Policy
Implication: Proactive set up of routing rules
F1
I1
F2
I2
Implication: New verification requirements
Notes: Here .. Sequence not just composition and spatial, not just single box/signle controller

## Slide 9: Flow rules may not suffice?
Firewall
Proxy
IDS
1
3
4
5
S1
S2
HTTP
HTTP: Firewall  IDS  Proxy
OpenFlow forward: Pkt header, Interface  Forwarding interface
2
Implication: More flexible forwarding abstractions
Return path?
Stateful!
HTTP, S1—S2  ??
Implication: loop-free at logical level, not physical

## Slide 10: Middlebox load balancing
S1
S5
S2
S3
S4
Src = 10.1.0.0/16
F1 = 0.5
I1 = 0.25
F2 =0.5
I2 = 0.75
10.1/16

*
Src, Dst, Input,NextHop
10.1.0/17,*,*,S2
10.1.128/17,*,*,S3
Src, Dst, Input,NextHop
10.1.128/17,*,S1,M3
10.1.128/17,*,M3,S4
Src, Dst, Input,NextHop
10.1.0/17,*,S1,M1
10.1.0/18,*,M1,M2
10.1.64/18,*,M1,S4
10.1.0/18,*,M2,S4
Src, Dst, Input,NextHop
10.1.0/18,*,S2,S5
10.1.64/18,*,S2,M4
10.1.128/17,*,S3,M4
10.1.64/18,*,M4,S5
10.1.128/17,*,M4,S5
Firewall
IDS
Policy
Implication: Unified view of MB and switch resources

## Slide 11: Middlebox introduce packet mods
NAT rewrites headers
Proxy, WanOPT coalesces sessions
Dynamic invocation?
Implication: Visibility and scalability challenges
Notes: Something like the conditional composition ..

## Slide 12: Middlebox implications for SDN view
Network OS
Data Plane
Control Apps
“Flow” | Action
… | …
Physical View
Logical view
Specify policy goals
Admin
MB + switch resources
Verification
Handle dynamics
More expressive
data plane fwding

## Slide 13: Roadmap
Motivation for this talk
Challenges with SDN-MB integration
Promising starts
Reflections..

## Slide 14: Middlebox implications for SDN view
Network OS
Data Plane
Control Apps
“Flow” | Action
… | …
Physical View
Logical view
Specify policy goals
Admin
MB + switch resources
Verification
Handle dynamics
More expressive
data plane fwding

## Slide 15: Logical view: “DataFlow” Abstraction
Firewall
WanOpt
Firewall
Proxy
Classifier
Public,
Web
Intranet,
NFS
Public,
Rest
“Raw”
Traffic
IDS
Specify “what” processing, not “where”

## Slide 16: Middlebox implications for SDN view
Network OS
Data Plane
Control Apps
“Flow” | Action
… | …
Physical View
Logical view
Specify policy goals
Admin
MB + switch resources
Verification
Handle dynamics
More expressive
data plane fwding

## Slide 17: Data plane: Virtual Packet State
Firewall
Proxy
IDS
1
3
4
5
S1
S2
HTTP
HTTP: Firewall  IDS  Proxy
2
Each segment gets a logical tag
Can implement this with VLAN tags/tunnels
Notes: Analogous to the virtual packet idea from jen -- @ controller, realization is via “VLAN” – packet carries its logical state somehow

## Slide 18: Middlebox implications for SDN view
Network OS
Data Plane
Control Apps
“Flow” | Action
… | …
Physical View
Logical view
Specify policy goals
Admin
MB + switch resources
Verification
Handle dynamics
More expressive
data plane fwding

## Slide 19: Joint configuration of MB + Switch
SDN-MB
Controller
Processing
Distribution
Topology,
Traffic
Policy
Spec
Resource
Constraints
Middlebox
behavior
Forwarding
Rules
Joint
optimization
Challenge: Impact of MB load balancing on switches?
  i.e., is a given load balancing strategy feasible?

## Slide 20: Idea: Enumerate physical sequences!
S1
S5
S2
S3
S4
Policy
F1
F2
I2
I1
F1-I1 : S1  S2  F1 S2  I1  S2  S4  S5 3 rules on S2, 1 on rest
F1-I2: S1  S2  F1  S2  S4  I2  S4  S5 2 rules on S2 & S4, 1 on rest
F2-I2: S1  S3  F2 S3  S4  I2  S4  S5 2 rules on S3, S4; 1 on rest
F2: I1: S1  S3  F2  S3  S1  S2  I1  S2 S4  S5 2 rules on S1, S2, S3
Not yet tractable (discrete optimization)

## Slide 21: Verification properties
Policy compliance: Every packet goes through correct policy
No extra processing: A packet should not traverse a middlebox, if the policy does not dictate it.
No spurious traffic:
Packets that would be dropped otherwise, should not be allowed
Have needs, don’t yet have solutions ..

## Slide 22: Dynamic middlebox transformations?
What we do know how to do
  Taxonomy of existing middleboxes
  Capture typical packet transformations
No comprehensive solution yet …

## Slide 23: Roadmap
Motivation for this talk
Challenges with SDN-MB integration
Promising starts
Reflections..

## Slide 24: Some reflections on SDN-MB synergy
Aug. 2012 ONF report on new initiatives
  integrate an SDN into production networks
  APIs for functions the market views as important
  Development of next generation forwarding plane
Middlebox as a concrete use-case can inform these initiatives!

## Slide 25: More reflections on SDN-MB synergy
Survey reports on key factors on SDN adoption [Metzler 2012]
  use cases that justify deployment ..
  fits in with both the existing infrastructure..
“ SDN tended to focus on the physical network elements that comprised the network layers (e.g., Layer 2 and Layer 3) …add a focus on Layer 4 through Layer 7 functionality … it shows a change in the perceived value of SDN.”
Middleboxes are a necessity and an opportunity!

## Slide 26: Talk summary
Can we achieve “incremental” SDN-MB integration?
Several challenges, but promising starts
  Composition, resource management, dynamics
  Implications for data, control plane, and control apps
MB can be an informative and concrete use-case
Longer-term evolution?
  SDN gets rid of MBs?
  MB becomes integrated into dataplane?