## Slide 1
Urban Influences on Temperature
in New Jersey
Dr. David A. Robinson Professor, Department of Geography
& New Jersey State Climatologist Rutgers University DIMACS/CCICADA Workshop on Urban Planning for Climate Events
September 23, 2013

## Slide 2
Outline
Urban climate
Urban heat island
Anatomy of the NJ/NY Metro heat island
  Geography
  Diurnal
  Seasonal
  Synoptic
  Heat waves
  Over time
What lies ahead

## Slide 3
http://www.ucar.edu/communications/staffnotes/0603/cities.shtml
Urban Climate

## Slide 4
Outline
Urban climate
Urban heat island
Anatomy of the NJ/NY Metro heat island
  Geography
  Diurnal
  Seasonal
  Synoptic
  Heat waves
  Over time
What lies ahead

## Slide 5: Urban Heat Islands
Urban heat island refers to the increased local temperatures that result from urbanization.
Occurs due to modifications to the energy balance that result when natural surfaces are paved and built upon or when human activities release heat into the environment.
Several variables influence the magnitude of the heat island: population density, radiation, changes in heat storage, sensible and latent heat transfer.

## Slide 6
Increased particulates associated with urban activity absorbs and scatters incoming solar radiation. May also reduce transfer of thermal radiation away from the urban environment.
Buildings, often a part of urbanized areas, impact the radiation balance by albedo and energy transfer.
Conduction and convection affect the energy balance to form urban heat island.
The release of heat from buildings plays a major role in urban heat islands.

## Slide 7
Late afternoon air temperature profile
across the urban environment and beyond

## Slide 10
Thuman, C.C., 2008. Summertime urban heat island in Newark, NJ and its relationship with urban particulate matter.
Rutgers master’s thesis
Frequency of maximum urban heat island intensity
at Newark for 80 summertime events

## Slide 11
Outline
Urban climate
Urban heat island
Anatomy of the NJ/NY Metro heat island
  Geography
  Diurnal
  Seasonal
  Synoptic
  Heat waves
  Over time
What lies ahead

## Slide 12
Mid Atlantic from space: enhanced infrared (thermal) image

## Slide 13
New Jersey from space:
visible composite image

## Slide 14
Paterson
Newark
Elizabeth
Trenton
Camden
New Jersey: enhanced infrared (thermal) image

## Slide 15
Elizabeth
Newark
Paterson
Center for Remote Sensing & Spatial Analysis, Rutgers University
ASTER TIR image of NJ centered on the Watchung Mountains, ASTER Band 12 (9.075 um) was acquired July 3, 2001. Daytime image.
Colors: Cold to warm to hot (blue to green to red).

## Slide 16
Trenton
Camden
cloud
cloud
Center for Remote Sensing & Spatial Analysis, Rutgers University
ASTER TIR image of NJ centered on Trenton, ASTER Band 12 (9.075 um) was
acquired July 3, 2001. Daytime image.
Colors: Cold to warm to hot (blue to green to red).

## Slide 17
Human Population Density in the Mid Atlantic

## Slide 18
NJ Weather and Climate Network (njwxnet.org)
Temperatures (deg F):
8AM EST,
January 29, 2005

## Slide 19
http://philiporton.com/2011/08/01/forecasting-coastal-urban-microclimates/
Metro NJ/NY temperatures at 1:15 AM: June 9, 2011

## Slide 20
Outline
Urban climate
Urban heat island
Anatomy of the NJ/NY Metro heat island
  Geography
  Diurnal
  Seasonal
  Synoptic
  Heat waves
  Over time
What lies ahead

## Slide 21
Thuman, C.C., 2008. Summertime urban heat island in Newark, NJ and its relationship with urban particulate matter.
Rutgers master’s thesis
Hourly frequency of heat island events:
Newark: June 10 – September 10, 2007

## Slide 22
Dawn and Late Afternoon Temperature Profiles

## Slide 23
Gedzelman et al., 2003. Mesoscale aspects of the urban heat island around New York City. Theoretical and Applied Climatology
Mean temperature (deg C) at midnight:
September – November 1998

## Slide 24
Gedzelman et al., 2003. Mesoscale aspects of the urban heat island around New York City. Theoretical and Applied Climatology
Two hour temperature change (deg C):
6 – 8 AM EST October 25, 1998

## Slide 25
Gedzelman et al., 2003. Mesoscale aspects of the urban heat island around New York City. Theoretical and Applied Climatology
Three hour temperature change (deg C):
3 – 6 PM EST December 9, 1998

## Slide 26
Thuman, C.C., 2008. Summertime urban heat island in Newark, NJ and its relationship with urban particulate matter.
Rutgers master’s thesis
Negative Heat Island in Newark:
June 10 – September 10, 2007

## Slide 27
Outline
Urban climate
Urban heat island
Anatomy of the NJ/NY Metro heat island
  Geography
  Diurnal
  Seasonal
  Synoptic
  Heat waves
  Over time
What lies ahead

## Slide 28
Gedzelman et al., 2003. Mesoscale aspects of the urban heat island around New York City. Theoretical and Applied Climatology
Seasonal urban – rural temperature difference
Fall
Summer
Winter
Spring

## Slide 29
Thuman, C.C., 2008. Summertime urban heat island in Newark, NJ and its relationship with urban particulate matter.
Rutgers master’s thesis
Maximum urban – rural temperature difference:
June 10 – September 10, 2007

## Slide 30
Thuman, C.C., 2008. Summertime urban heat island in Newark, NJ and its relationship with urban particulate matter.
Rutgers master’s thesis
Urban &rural humidity during
80 summer heat island events

## Slide 31
Outline
Urban climate
Urban heat island
Anatomy of the NJ/NY Metro heat island
  Geography
  Diurnal
  Seasonal
  Synoptic
  Heat waves
  Over time
What lies ahead

## Slide 32
Gedzelman et al., 2003. Mesoscale aspects of the urban heat island around New York City. Theoretical and Applied Climatology
Fraction of cases with urban – rural temperature
differences at given values for clear & overcast conditions

## Slide 33
Thuman, C.C., 2008. Summertime urban heat island in Newark, NJ and its relationship with urban particulate matter.
Rutgers master’s thesis
Daily rainfall and urban heat island intensity:
June 10 – September 10, 2007

## Slide 34
Gedzelman et al., 2003. Mesoscale aspects of the urban heat island around New York City. Theoretical and Applied Climatology
Average urban – rural temperature difference
for each night following a cold front passage

## Slide 35
Temperatures:
4PM EDT,
April 11, 2011
NJ Weather and Climate Network (njwxnet.org)

## Slide 36
Holzer, M.A., 2004. Synoptic and diurnal characteristics of the northern NJ heat island, Rutgers master’s thesis

## Slide 37: Winter SSC’s at All Stations
Chart: Dry Polar Winter All Stations
| Hour 1 | Hour 2 | Hour 3 | Hour 4 | Hour 5 | Hour 6 | Hour 7 | Hour 8 | Hour 9 | Hour 10 | Hour 11 | Hour 12 | Hour 13 | Hour 14 | Hour 15 | Hour 16 | Hour 17 | Hour 18 | Hour 19 | Hour 20 | Hour 21 | Hour 22 | Hour 23 | Hour 24
Eliz-Chatham | 2.6486 | 2.8108 | 2.8919 | 2.8919 | 2.973 | 3 | 3.0811 | 2.9324 | 2.3649 | 1.0811 | 0.31081 | 0.85243 | -0.47297 | -0.48649 | 0.98649 | 1.3784 | 1.6081 | 2 | 2.3514 | 2.5 | 2.6081 | 2.8649 | 2.8243 | 3.0135
Eliz-BM | 3.7541 | 3.823 | 3.8851 | 3.673 | 3.6541 | 3.8243 | 4.0473 | 2.4662 | 0.14324 | -0.67568 | -0.67027 | -0.05027 | -0.72027 | 0.022973 | 0.88243 | 0.75405 | 1.7189 | 2.8473 | 3.6081 | 4.3189 | 4.5514 | 4.7608 | 4.8041 | 4.8838
Eliz-Hacketts | 5.3216 | 5.5351 | 5.4392 | 5.4865 | 5.6243 | 5.7135 | 5.8014 | 4.873 | 2.5851 | 2.1541 | 2.0081 | 2.4538 | 1.0865 | 0.81622 | 1.6878 | 2.6122 | 3.6297 | 4.2743 | 4.9081 | 5.1514 | 5.6324 | 5.7905 | 5.6527 | 5.9041
Eliz-Stw | 5.7514 | 5.8851 | 5.5284 | 5.8378 | 6.0432 | 5.9095 | 6.023 | 4.6095 | 0.36486 | -1.0689 | -1.1581 | -0.54757 | -0.091892 | 0.14459 | 0.43649 | 1.3216 | 3.1432 | 4.2824 | 5.4 | 5.7351 | 5.9811 | 6.1432 | 5.8595 | 6.1311
Eliz-Want | 6.7811 | 6.7581 | 6.7919 | 6.4649 | 6.5716 | 6.5095 | 6.8432 | 6.0757 | 5.0486 | 3.5338 | 3.4676 | 3.9673 | 3.1324 | 3.8297 | 5.3068 | 5.8243 | 6.8297 | 7.4095 | 7.7459 | 7.7527 | 7.6432 | 7.6068 | 7.3257 | 7.1108
Eliz-No Hale | 3.5878 | 3.6311 | 3.5365 | 3.2203 | 3.3527 | 3.4878 | 3.5595 | 3.4649 | 2.7527 | 2.2122 | 1.3054 | 2.3849 | 1.4784 | 0.36216 | 1.1743 | 1.6649 | 2.6608 | 3.5473 | 4.0162 | 4.1892 | 4.2527 | 4.1932 | 3.9959 | 4.0095
Chart: Moist Polar Winter All Stations
| Hour 1 | Hour 2 | Hour 3 | Hour 4 | Hour 5 | Hour 6 | Hour 7 | Hour 8 | Hour 9 | Hour 10 | Hour 11 | Hour 12 | Hour 13 | Hour 14 | Hour 15 | Hour 16 | Hour 17 | Hour 18 | Hour 19 | Hour 20 | Hour 21 | Hour 22 | Hour 23 | Hour 24
Eliz-Chatham | 1.6429 | 2.1786 | 2.0357 | 2.1071 | 2.0357 | 2.1429 | 2.5 | 2.25 | 1.7857 | 1.4643 | 1.1786 | 0.85714 | 0.67857 | 0.85714 | 1 | 1.5714 | 1.6429 | 1.8214 | 1.8571 | 2.1786 | 2.0714 | 2.0357 | 2.0357 | 2.0357
Eliz-BM | 2.0286 | 2.6036 | 2.3714 | 2.2857 | 1.9036 | 1.6821 | 2.0893 | 1.75 | 1.0143 | 0.65714 | 0.20357 | -0.17857 | -0.16429 | 0.092857 | 0.46786 | 0.86429 | 1.3357 | 1.6857 | 1.6143 | 2.0857 | 1.9714 | 1.9679 | 1.5857 | 1.5429
Eliz-Hacketts | 3.7821 | 4.2786 | 3.9429 | 4.0321 | 3.7607 | 3.8429 | 4.0464 | 3.5536 | 3.1357 | 2.3571 | 2.1571 | 1.7214 | 1.85 | 2.0929 | 2.25 | 2.6893 | 2.8429 | 2.8429 | 2.7036 | 3.2821 | 3.4 | 3.55 | 3.5929 | 3.8357
Eliz-Stw | 3.4893 | 3.6 | 3.3893 | 3.3786 | 3.0643 | 3.0679 | 3.1607 | 2.3929 | 2.125 | 1.9321 | 1.1964 | 0.93929 | 1.0179 | 1.0679 | 1.2357 | 1.5893 | 2.0571 | 2.2714 | 2.3821 | 2.9321 | 3.3179 | 3.375 | 3.2 | 3.5393
Eliz-Want | 6.5357 | 6.7571 | 6.7429 | 6.7357 | 6.5786 | 6.5893 | 6.9893 | 6.5929 | 6.0286 | 5.7714 | 5.375 | 5.2321 | 5.2036 | 5.7893 | 5.9393 | 6.4107 | 6.5393 | 6.675 | 6.6929 | 7.0036 | 6.7357 | 7.0286 | 6.7786 | 6.7571
Eliz-No Hale | 3.0179 | 3.3964 | 3.2321 | 3.4929 | 3.0714 | 3.05 | 3.475 | 3.1929 | 2.6393 | 2.275 | 2.1321 | 1.9643 | 2.0393 | 2.0321 | 2.2857 | 2.8071 | 3.0214 | 3.325 | 3.1393 | 3.575 | 3.3929 | 3.625 | 3.375 | 3.0929
Chart: Dry Moderate Winter All Stations
| Hour 1 | Hour 2 | Hour 3 | Hour 4 | Hour 5 | Hour 6 | Hour 7 | Hour 8 | Hour 9 | Hour 10 | Hour 11 | Hour 12 | Hour 13 | Hour 14 | Hour 15 | Hour 16 | Hour 17 | Hour 18 | Hour 19 | Hour 20 | Hour 21 | Hour 22 | Hour 23 | Hour 24
Eliz-Chatham | 2.0565 | 2.2328 | 2.1999 | 2.1238 | 2.0473 | 2.0673 | 2.0857 | 2.0665 | 1.627 | 0.013498 | -0.47985 | -0.038928 | -1.3042 | -1.3212 | 0.27836 | 0.7768 | 1.0256 | 1.5722 | 1.7079 | 1.9914 | 2.09 | 2.4679 | 2.3388 | 2.5012
Eliz-BM | 4.4861 | 4.2042 | 4.0111 | 4.2889 | 4.7347 | 4.6569 | 4.8319 | 3.3708 | 0.19028 | -1.1667 | -1.3125 | -0.95556 | -1.5264 | -1.1486 | -0.28889 | -0.29444 | 1.3014 | 3.7292 | 4.8806 | 5.1694 | 5.6875 | 5.8528 | 5.5389 | 5.5417
Eliz-Hacketts | 5.0556 | 5.2181 | 5.2583 | 5.275 | 5.2528 | 5.2972 | 5.5264 | 4.8917 | 2.3417 | 1.2833 | 1.3389 | 1.8083 | 0.61389 | 0.50139 | 1.2694 | 2.0472 | 3.6708 | 5.1222 | 5.5833 | 5.8472 | 5.7958 | 5.6875 | 5.3125 | 5.0361
Eliz-Stw | 5.3083 | 5.5736 | 5.7222 | 5.7 | 5.975 | 5.9944 | 6.3444 | 4.9542 | 0.94444 | -0.86944 | -0.9 | -0.15139 | -0.25139 | 0.13333 | -0.13889 | 0.65833 | 2.9069 | 5.4792 | 5.8208 | 5.6847 | 5.6972 | 5.5431 | 5.3958 | 5.3583
Eliz-Want | 4.5611 | 4.5792 | 4.2 | 4.125 | 3.8583 | 3.8458 | 4.0264 | 3.4792 | 2.1236 | 1.4903 | 2.5069 | 3.6514 | 3.1944 | 4.0014 | 5.0194 | 5.4764 | 6.5181 | 6.9139 | 6.1597 | 5.7333 | 5.3722 | 5.1264 | 4.8931 | 4.8097
Eliz-No Hale | 2.7347 | 2.7194 | 2.5181 | 2.5153 | 2.3375 | 2.4736 | 2.8625 | 2.8278 | 2.2681 | 1.5486 | 1.0014 | 2.1931 | 1.475 | 0.44028 | 0.98889 | 1.6528 | 2.5458 | 3.6639 | 3.6514 | 3.5111 | 3.4333 | 3.1389 | 3.0236 | 2.8639
Chart: Moist Moderate Winter All Stations
| Hour 1 | Hour 2 | Hour 3 | Hour 4 | Hour 5 | Hour 6 | Hour 7 | Hour 8 | Hour 9 | Hour 10 | Hour 11 | Hour 12 | Hour 13 | Hour 14 | Hour 15 | Hour 16 | Hour 17 | Hour 18 | Hour 19 | Hour 20 | Hour 21 | Hour 22 | Hour 23 | Hour 24
Eliz-Chatham | 1.5 | 1.2333 | 1.3667 | 1.2667 | 1.5 | 1.5667 | 1.5 | 1.5 | 1.2 | 0.66667 | 0.46667 | 0.7 | 0.43333 | 0.76667 | 0.66667 | 0.86667 | 1.1333 | 1.3667 | 1.1667 | 1.3333 | 1.2667 | 1.0667 | 1.2333 | 1.2667
Eliz-BM | 2.1067 | 2.1567 | 2.3933 | 2.4067 | 2.5367 | 2.5033 | 2.3867 | 1.68 | 1.1167 | 0.43 | -0.02 | 0.2 | 0.20333 | 0.80667 | 0.44333 | 0.52333 | 1.14 | 1.9433 | 1.5967 | 1.5433 | 1.4833 | 1.0633 | 1.1933 | 1.7267
Eliz-Hacketts | 3.0333 | 2.43 | 2.3767 | 2.48 | 2.6533 | 2.98 | 2.7333 | 2.4433 | 1.8633 | 1.2767 | 1.9633 | 2.3767 | 2.1933 | 2.4467 | 1.68 | 1.9367 | 2.6 | 2.8667 | 2.7867 | 2.6933 | 2.55 | 2.1233 | 2.26 | 2.53
Eliz-Stw | 2.28 | 1.8767 | 1.8233 | 1.96 | 2.64 | 2.9867 | 3.2367 | 3.16 | 1.4667 | 0.39333 | 0.71333 | 1.31 | 1.74 | 1.4733 | 0.69333 | 0.87667 | 1.4967 | 2.05 | 1.77 | 1.64 | 1.49 | 1.36 | 1.7267 | 1.7067
Eliz-Want | 4.9567 | 4.4733 | 4.48 | 4.4233 | 4.6033 | 4.6933 | 4.5633 | 4.1867 | 3.5567 | 3.5033 | 4.31 | 4.8267 | 5.0367 | 5.4733 | 5.0633 | 5.3433 | 5.85 | 5.78 | 5.4633 | 5.2867 | 5.31 | 4.8933 | 4.8633 | 4.9867
Eliz-No Hale | 2.75 | 2.4633 | 2.46 | 2.28 | 2.5633 | 2.54 | 2.3867 | 2.39 | 2.0733 | 1.6733 | 1.68 | 2.17 | 2.05 | 2.1767 | 2.0667 | 2.4467 | 3.0767 | 3.3533 | 3.0767 | 3.2333 | 3.25 | 3.0167 | 2.9867 | 2.9533
Holzer, M.A., 2004. Synoptic and diurnal characteristics of the northern NJ heat island, Rutgers master’s thesis
Notes: *Quick cooling at hour 12 under dry conditions may be artificial induced warming at Elizabeth
*Wantage cools after hour 10 under dry moderate conditions, and after hour 13 under dry polar conditions – may be because of daytime orographic produced cloud cover

## Slide 38: Dry Moderate SSC in All Seasons at Belle Mead and Chatham
Inversion at Belle Mead breaks between hours 7 and 9 in all seasons
Timing of evening cool down is dependent on the time of sunset
During the overnight hours Chatham is warmer than Belle Mead
Chart: Chatham Dry Moderate SSC in All Seasons
| Hour 1 | Hour 2 | Hour 3 | Hour 4 | Hour 5 | Hour 6 | Hour 7 | Hour 8 | Hour 9 | Hour 10 | Hour 11 | Hour 12 | Hour 13 | Hour 14 | Hour 15 | Hour 16 | Hour 17 | Hour 18 | Hour 19 | Hour 20 | Hour 21 | Hour 22 | Hour 23 | Hour 24
Eliz-CH Winter | 2.0565 | 2.2328 | 2.1999 | 2.1238 | 2.0473 | 2.0673 | 2.0857 | 2.0665 | 1.627 | 0.013498 | -0.47985 | -0.038928 | -1.3042 | -1.3212 | 0.27836 | 0.7768 | 1.0256 | 1.5722 | 1.7079 | 1.9914 | 2.09 | 2.4679 | 2.3388 | 2.5012
Eliz-CH Spring | 3.1 | 3.4333 | 3.5 | 3.9667 | 3.9333 | 3.8667 | 3.7667 | 3.3667 | 1.0667 | 0.033333 | 0.1 | 0.066667 | -0.3 | 0.066667 | 0.26667 | -0.066667 | -0.26667 | -0.4 | 0.2 | 1.3333 | 1.9333 | 1.9333 | 2.2333 | 2.6
Eliz-CH Summer | 3.5667 | 3.2333 | 3.4333 | 3.7333 | 3.7667 | 3.5 | 4 | 4.0333 | 1.8 | 0.43333 | 0.033333 | -0.26667 | -0.066667 | -0.3 | -0.26667 | -1.5333 | -2.2 | -2.9333 | -2.6333 | 0.066667 | 2.2333 | 3.0333 | 3.1333 | 3.1
Eliz-CH Fall | 3.3103 | 3.5862 | 3.3448 | 2.8966 | 3 | 3.4138 | 3.3793 | 3.4828 | 2.2414 | 0.068966 | -0.44828 | -0.27586 | -0.86207 | -0.82759 | -0.55172 | 1 | 1.1034 | 1.5517 | 2.5862 | 3.3103 | 3.2759 | 3.5862 | 3.6207 | 3.6207
Chart: Belle Mead Dry Moderate SSC in All Seasons
| Hour 1 | Hour 2 | Hour 3 | Hour 4 | Hour 5 | Hour 6 | Hour 7 | Hour 8 | Hour 9 | Hour 10 | Hour 11 | Hour 12 | Hour 13 | Hour 14 | Hour 15 | Hour 16 | Hour 17 | Hour 18 | Hour 19 | Hour 20 | Hour 21 | Hour 22 | Hour 23 | Hour 24
Eliz-BM Winter | 4.4861 | 4.2042 | 4.0111 | 4.2889 | 4.7347 | 4.6569 | 4.8319 | 3.3708 | 0.19028 | -1.1667 | -1.3125 | -0.95556 | -1.5264 | -1.1486 | -0.28889 | -0.29444 | 1.3014 | 3.7292 | 4.8806 | 5.1694 | 5.6875 | 5.8528 | 5.5389 | 5.5417
Eliz-BM Spring | 7.08 | 7.12 | 6.7967 | 7.35 | 7.4867 | 7.46 | 5.5667 | 1.9233 | 0.61333 | 0.45333 | 0.23667 | 0.10333 | -0.57333 | 0.31333 | 0.33333 | -0.36667 | -0.79 | -0.56 | 1.3133 | 3.1867 | 4.2767 | 4.4767 | 5.2567 | 5.8433
Eliz-BM Summer | 7.5633 | 7.69 | 7.8367 | 7.5833 | 7.48 | 7.3067 | 5.54 | 2.0233 | 0.2 | -0.68333 | -1.0667 | -1.1633 | -0.83333 | -1.1267 | -0.91333 | -1.9467 | -3.19 | -3.3533 | -2.3133 | 1.4433 | 4.74 | 5.8533 | 5.95 | 6.0833
Eliz-BM Fall | 6.3276 | 6.7207 | 6.1724 | 6.3414 | 6.4483 | 6.1172 | 6.4828 | 3.0276 | 0.21034 | -0.84828 | -1.2793 | -1.1586 | -1.5966 | -1.131 | -0.8931 | -0.18621 | 0.28621 | 1.6241 | 4.6552 | 7.1759 | 6.8724 | 6.9483 | 6.6862 | 6.9517
Holzer, M.A., 2004. Synoptic and diurnal characteristics of the northern NJ heat island, Rutgers master’s thesis
Notes: Urban influence see in Chatham, not in Belle Mead

## Slide 39
Holzer, M.A., 2004. Synoptic and diurnal characteristics of the northern NJ heat island, Rutgers master’s thesis
Winter 4 AM: Dry Moderate

## Slide 40
Holzer, M.A., 2004. Synoptic and diurnal characteristics of the northern NJ heat island, Rutgers master’s thesis
Summer noon: Dry Moderate

## Slide 41
Outline
Urban climate
Urban heat island
Anatomy of the NJ/NY Metro heat island
  Geography
  Diurnal
  Seasonal
  Synoptic
  Heat waves
  Over time
What lies ahead

## Slide 42
Li and Bou-Seid, 2013. Synergistic interactions between urban heat islands and heat waves: the impact in cities is larger than
The sum of its parts. Journal of Applied Meteorology and Climatology
Synergistic interaction mechanisms between the
urban heat island and heat waves

## Slide 43
Newark, NJ and vicinity
Google maps

## Slide 44
Office of the NJ State Climatologist

## Slide 45
Office of the NJ State Climatologist

## Slide 46
Office of the NJ State Climatologist

## Slide 47
Office of the NJ State Climatologist

## Slide 48
Office of the NJ State Climatologist

## Slide 49
Office of the NJ State Climatologist

## Slide 50
Office of the NJ State Climatologist

## Slide 51
Office of the NJ State Climatologist

## Slide 52
Outline
Urban climate
Urban heat island
Anatomy of the NJ/NY Metro heat island
  Geography
  Diurnal
  Seasonal
  Synoptic
  Heat waves
  Over time
What lies ahead

## Slide 53
1931
2012

## Slide 54
1931
2012

## Slide 55
Outline
Urban climate
Urban heat island
Anatomy of the NJ/NY Metro heat island
  Geography
  Diurnal
  Seasonal
  Synoptic
  Heat waves
  Over time
What lies ahead

## Slide 56
The heat index combines the effects of temperature and humidity to estimate human comfort.
Results are from simulations with three global climate models with two emissions scenarios, representing the low and high ends of the IPCC range.
Under the high emissions scenario, Tri-State summers at the end of the 21st century are projected to be similar to those in Savannah, Georgia today.
Changes in heat index

## Slide 57
days per year over 90ºF
days per year over 100ºF
Union of Concerned Scientists, NE Climate Impacts Report, 2006
Days over 90F
Days over 100F
Projected warming

## Slide 58
Rising temperatures
Steady or increasing precipitation
Increasing variability and extremes
    - storms, flood, drought, heat…….
Rising sea level
New Jersey's future climate

## Slide 59
Wrapping things up:
Anatomy of the NJ/NY Metro heat island
  Geography
  Diurnal
  Seasonal
  Synoptic
  Heat waves
  Over time
What lies ahead
Thanks: Dave Robinson
      david.robinson@rutgers.edu